## Slide 1
Methane emission reduction technology by the combination of biogas effluent application and multiple drainage in a rice paddy
The technology which combing biogas effluent application and multiple drainage could reduce methane (CH4) emission from rice paddy fields without yield loss, as compared to the local conventional practice.
Agriculture, Forestry and Fisheries Technology Catalog for the Asia-Monsoon region
本文のフォントは11p
行間は1.2倍で固定
字間は標準
両端揃え
詳細情報
URLとQRコードを併記。
QRコードは次で生成可。
https://m.qrqrq.com/
位置は図表に合わせて左右どちらに寄せても良い。
本文のフォントは11p 「Segoe UI」を使用
行間は1.2倍で固定
字間は標準
両端揃え
Production
Item: Paddy rice
Demonstration
Fig.1. The technology proposed to reduce CH4 emission from rice paddy fields without yield loss.
Biogas digester
Conventional
Proposed
Fig.2. Comparison between the proposed combination technology and conventional practice.
GWP: CO2-equivalent of combined CH4 and N2O emissions
Ratio to conventional practice (％）
Technical details:
Outline
The technology which combines cattle biogas effluent as fertilizer and multiple drainage could reduce 1) greenhouse gas emission from rice paddy fields and 2) environmental problem caused by the discharge of untreated biogas effluent into rivers. In the triple-rice cropping system in Mekong Delta in Vietnam, the technology with each of two multiple drainage practices, AWD*, a water-depth-dependent irrigation, and MiDi, a day-number-dependent irrigation (Fig.1) reduced CH4 emission by 11-13% and nitrous oxide (N2O) emission by 35-54% without yield loss (Fig.2).
The proposed technology can be applied to the rice-producing areas using livestock biogas effluent as fertilizer.
Background/effect/note
Japan International Research
Center for Agricultural Sciences
*AWD (alternate wetting and drying) and MiDi (Midseason drainage followed by intermittent irrigation) are water management practices with a combined effect of water-saving by repeatedly flooding and draining water in paddy fields, and reduction of CH4 emission by increasing the oxygen concentration in the soil.
図表キャプション
10p、行間は1倍で固定
両端揃え
https://www.jircas.go.jp/ja/publication/research_results/2021_a01
左右余白は15mm確保
（冊子版綴じ代）
左右余白は15mm確保
（冊子版綴じ代）
Production
-----
Procurement
----------
Consumption
----------
Processing and
distribution
-------------
対象とする食料サプライチェーンの段階に合わせて、(a)～(d)の１つをセットで使用
(a)
(b)
(c)
(d)
専門用語を使う必要があれば、近傍に注釈を入れる。
下余白は15mm確保
（ページ番号挿入予定）
タイトル領域4cm
タイトルのフォントは18pt太字
英文タイトルは下揃えで3行以内
英語版では、段落の間は行間を空ける。段落後3pt。
上余白10mm確保
英文フォントは「Segoe UI」を使用
GHG emission reduction